Coversheet

The Coversheet must contain the following:

- Heading “Electrical System Form FSEast 2017”

- University and Team Name

- Car number

- Main Team Contact for ESF related questions

Feel free to add team logo, car picture, and the like.

Requirements (delete this section after you have read and understood it):

Read the document “How to complete ESF” which is available at:
https://www.fsaeonline.com/content/How-to-Complete-ESF.pptx

Maximum number of pages for the complete ESF is 100 pages!

Links to video or audio data are prohibited.

If you did not fill out the tables or if you changed the format of the ESF Template, you will fail by default.

Every single part/heading of the ESF Template must be filled with content. If the respective part is not relevant for your concept, describe shortly why not.

The table of contents must be hyperlinked.

The generated PDF must contain hyperlinked bookmarks.

Use internal reference links. For example, when describing wiring and mentioning a figure in the text then link it to the figure.

Do not just copy all your datasheets in the appendix, e.g. we do not need to know what you must do to program your motor controller; we do not need the whole user manuals of microcontrollers to review your ESF, etc.  Similarly, do not just paste only a link to the entire data sheet.  We should not need an internet connection to obtain the information necessary to review your ESF.

Single pages/figures/tables extracted from the complete datasheet showing the important parameters, figures, etc. are usually sufficient, but the source/link to the complete datasheet must be provided. If the datasheet describes more than one type, clearly mark in the datasheet to which type you are referring / which type you plan to use.

Datasheets should only be used as a reference. Please cover the important data in your text by using tables, figures, etc.

If you refer to parts of a data sheet, then you need to provide an internal document links from the text to the respective datasheet and another internal document link back from the datasheet to the text section.
For example a link in the motor controller section “The datasheet can be found here (clickable)” and a link above the motor controller datasheet in the appendix “The section covering the motor controller can be found here (clickable)”.

If you are unsure with respect to feedback of the reviewer, do not hesitate to write an e-mail and ask.

Parts of the ESF which are changed because of reviewer’s feedback must be marked in red.

Following these guidelines will guarantee a swift review process.

Table of Contents

Table of Contents	iii

I	List of Figures	vii

II	List of Tables	viii

III	List of Abbreviations	ix

1	System Overview	2

2	Electrical Systems	3

2.1	Shutdown Circuit	3

2.1.1	Description/concept	3

2.1.2	Wiring / additional circuitry	3

2.1.3	Position in car	4

2.2	IMD	4

2.2.1	Description (type, operation parameters)	4

2.2.2	Wiring/cables/connectors/	5

2.2.3	Position in car	5

2.3	Inertia Switch	5

2.3.1	Description (type, operation parameters)	5

2.3.2	Wiring/cables/connectors/	5

2.3.3	Position in car	5

2.4	Brake Plausibility Device	5

2.4.1	Description/additional circuitry	5

2.4.2	Wiring	6

2.4.3	Position in car/mechanical fastening/mechanical connection	6

2.5	Reset / Latching for IMD and AMS	6

2.5.1	Description/circuitry	6

2.5.2	Wiring/cables/connectors	6

2.5.3	Position in car	6

2.6	Shutdown System Interlocks	7

2.6.1	Description/circuitry	7

2.6.2	Wiring/cables/connectors	7

2.6.3	Position in car	7

2.7	Tractive system active light	7

2.7.1	Description/circuitry	7

2.7.2	Wiring/cables/connectors	8

2.7.3	Position in car	8

2.8	Measurement points	8

2.8.1	Description	8

2.8.2	Wiring, connectors, cables	8

2.8.3	Position in car	8

2.9	Pre-Charge circuitry	8

2.9.1	Description	8

2.9.2	Wiring, cables, current calculations, connectors	8

2.9.3	Position in car	9

2.10	Discharge circuitry	9

2.10.1	Description	9

2.10.2	Wiring, cables, current calculations, connectors	9

2.10.3	Position in car	10

2.11	HV Disconnect (HVD)	10

2.11.1	Description	10

2.11.2	Wiring, cables, current calculations, connectors	10

2.11.3	Position in car	10

2.12	Ready-To-Drive-Sound (RTDS)	11

2.12.1	Description	11

2.12.2	Wiring, cables, current calculations, connectors	11

2.12.3	Position in car	11

3	Accumulator	12

3.1	HV Accumulator pack	12

3.1.1	Overview/description/parameters	12

3.1.2	Cell description	12

3.1.3	Cell configuration	13

3.1.4	Cell temperature monitoring	13

3.1.5	Accumulator Management System	13

3.1.6	Accumulator indicator	14

3.1.7	Wiring, cables, current calculations, connectors	14

3.1.8	Accumulator insulation relays	14

3.1.9	Fusing	15

3.1.10	Charging	16

3.1.11	Mechanical Configuration/materials	17

3.1.12	Position in car	17

3.2	GLVS Accumulator	17

4	Energy meter mounting	18

4.1	Description	18

4.2	Wiring, cables, current calculations, connectors	18

4.3	Position in car	18

5	Motor controller	19

5.1	Motor controller 1	19

5.1.1	Description, type, operation parameters	19

5.1.2	Wiring, cables, current calculations, connectors	19

5.1.3	Position in car	20

5.2	Motor controller 2	20

6	Motors	21

6.1	Motor 1	21

6.1.1	Description, type, operating parameters	21

6.1.2	Wiring, cables, current calculations, connectors	21

6.1.3	Position in car	22

6.2	Motor 2	22

7	Torque encoder	23

7.1	Description/additional circuitry	23

7.2	Torque Encoder Plausibility Check	23

7.3	Wiring	23

7.4	Position in car/mechanical fastening/mechanical connection	23

8	Additional LV-parts interfering with the tractive system	24

8.1	LV part 1	24

8.1.1	Description	24

8.1.2	Wiring, cables,	24

8.1.3	Position in car	24

8.2	LV part 2	24

9	Overall Grounding Concept	25

9.1	Description of the Grounding Concept	25

9.2	Grounding Measurements	25

10	Firewall(s)	26

10.1	Firewall 1	26

10.1.1	Description/materials	26

10.1.2	Position in car	26

10.2	Firewall 2	26

11	Appendix	27

# List of Figures

Has to be hyperlinked!

# List of Tables

Table 1.1 General parameters	2

Table 2.1 List of switches in the shutdown circuit	3

Table 2.2 Wiring – Shutdown circuit	4

Table 2.3 Parameters of the IMD	4

Table 2.4 Parameters of the Inertia Switch	5

Table 7.1 Torque encoder data	6

Table 2.6 Parameters of the TSAL	7

Table 2.7 General data of the pre-charge resistor	9

Table 2.8 General data of the pre-charge relay	9

Table 2.9 General data of the discharge circuit	10

Table 3.1 Main accumulator parameters	12

Table 3.2 Main cell specification	13

Table 3.5 Wire data of company A, 0.205 mm²	14

Table 3.3 Basic AIR data	15

Table 3.4 Basic fuse data	15

Table 3.5 Fuse Protection Table	16

Table 3.6 General charger data	17

Table 5.1 General motor controller data	19

Table 5.2 Wire data of company A, 0.205 mm²	20

Table 6.1 General motor data	21

Table 7.1 Torque encoder data	23

Has to be hyperlinked!

# List of Abbreviations

# System Overview

- Short description of the system’s concept

- Rough Schematic (blocks) showing all parts affected with the electrical systems and function of the tractive-system

- No detailed wiring

- Additionally, fill out the following table, replacing the values with your specifications:

| Maximum Tractive-system voltage: | for example: 600VDC |
| --- | --- |
| Nominal Tractive-system voltage: | for example: 560VDC |
| Control-system voltage: | for example: 12VDC, 24VDC |
| Accumulator configuration: | for example: 200s3p |
| Total Accumulator capacity: | for example: 200Ah |
| Nominal HV Accumulator current: |  |
| Maximum HV Accumulator current: |  |
| HV accumulator cell type: |  |
| LV Accumulator cell type: |  |
| Motor type: | for example: Permanent excitated synchronous motor |
| Number of motors: | for example: Total 4, one per wheel |
| Maximum combined motor power in kW | for example: 150 |

Table 1.1 General parameters

# Electrical Systems

## Shutdown Circuit

### Description/concept

Describe your concept of the shutdown circuit, the master switches, shut down buttons, brake over travel switch, etc.

Additionally, fill out the following table replacing the values with your specification and append additional switches from your setup:

| Part | Function |
| --- | --- |
| for example: Main Switch (for control and tractive-system; CSMS, TSMS) | for example: Normally open |
| for example: Brake over travel switch (BOTS) | for example: Normally closed |
| for example: Shutdown buttons (SDB) | for example: Normally closed |
| for example: Insulation Monitoring Device (IMD) | for example: Normally open |
| for example: Accumulator Management System (AMS) | for example: Normally open |
| for example: Inertia Switch | for example: Normally closed |
| for example: Interlocks | for example: Closed when circuits are connected |
| for example: Brake System Plausibility Device | for example: Normally Closed |

Table 2.1 List of switches in the shutdown circuit

### Wiring / additional circuitry

Describe wiring and additional circuitry, show extra schematics for example if additional transistors etc. are used, also describe the function of additional circuitry and make good use of figures.

Additionally, fill out and add information to the following table:

| Total Number of AIRs: | for example: 10 |
| --- | --- |
| Current per AIR: | for example: 0.5A |
| Additional parts consumption within the shutdown circuit: | for example: 2A |
| Total current: | for example: 7A |
| Cross sectional area of the wiring used: | for example: 0.205 mm² |

Table 2.2 Wiring – Shutdown circuit

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the renderings, if necessary.

## IMD

### Description (type, operation parameters)

Describe the IMD used and use a table for the common operation parameters, like supply voltage, set point, etc. Also, describe how the IMD indicator light is wired, etc.

Additionally, fill out the following table replacing the values with your specification:

| Supply voltage range: | for example: 10..36VDC |
| --- | --- |
| Supply voltage | for example: 24VDC |
| Environmental temperature range: | for example: -40..105°C |
| Selftest interval: | for example: Always at startup, then every 20 minutes |
| High voltage range: | for example: DC 0..1000V |
| Set response value: | for example: 300kΩ (500Ω/Volt) |
| Max. operation current: | for example: 500mA |
| Approximate time to shut down at 50% of the response value: | for example: 27s |

Table 2.3 Parameters of the IMD

### Wiring/cables/connectors/

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring including wire gauge/temp/voltage rating and fuses protecting the wiring.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Inertia Switch

### Description (type, operation parameters)

Describe the Inertia Switch used and use a table for the common operation parameters, like supply voltage, temperature, etc.

Additionally, fill out the following table replacing the values with your specification:

| Inertia Switch type: | for example: Sensata XYZ |
| --- | --- |
| Supply voltage range: | for example: 10..36VDC |
| Supply voltage: | for example: 12VDC |
| Environmental temperature range: | for example: -40..105°C |
| Max. operation current: | for example: 500mA |
| Trigger characteristics: | for example: 6g for 50ms / 11g for 15ms |

Table 2.4 Parameters of the Inertia Switch

### Wiring/cables/connectors/

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Brake Plausibility Device

## Description/additional circuitry

Describe how your electronic hardware brake plausibility system works (this is in addition to your ECU controlled brake plausibility software), provide tables with main operation parameters, and describe additional circuitry used to check or for an implausibility. Describe how the system reacts if an implausibility or error is detected.

| Brake sensor used: | for example: ABC Sensor |
| --- | --- |
| Brake sensor physical response value: |  |
| Tractive system power sensor type |  |
| Tractive system sensor physical response value: |  |
| Tractive System power sensor current treshold (5kW/Nominal TS voltage): |  |
| Supply voltages: | for example: 5V |
| Maximum supply currents: | for example: 20mA |
| Operating temperature: | for example: -20..180 °C |
| Output used to control AIRs: | for example: Open a relay |

Table 2.5 BSPD data

## Schematic

Describe the wiring, show schematics including the circuit board, show data regarding the cables and connectors used.

## Connenction with the shutdown circuit

Show how the device open the shutdown circuit.

## Position in car/mechanical fastening/mechanical connection

Provide CAD-renderings showing all relevant parts and discuss the mechanical connection of the sensors to the pedal assembly. Mark the parts in the rendering, if necessary.

## Reset / Latching for IMD and AMS

### Description/circuitry

Describe the concept and circuitry of the latching/reset system for a tripped IMD or AMS.  Describe the method for resetting the IMD and AMS.

### Wiring/cables/connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.  If not detailed in section 2.1, be sure to show how the device opens the shutdown circuit.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Shutdown System Interlocks

### Description/circuitry

Describe the concept and circuitry of the Shutdown System Interlocks.

Note: Interlocks are circuits used to open the shutdown circuit if a connector is disconnected or enclosure is opened.  This is not the entire shutdown circuit.

### Wiring/cables/connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Tractive system active light

### Description/circuitry

Describe the tractive system active light and additional circuitry.

Additionally, fill out the table:

| Supply voltage: | for example: 12VDC |
| --- | --- |
| Max. operational current: | for example: 700mA |
| Lamp type | for example: LED |
| Power consumption: | for example: 4.5 W |
| Brightness | for example: 100 Lumen |
| Frequency: | for example: 1.5Hz |
| Size (length x height x width): | for example: 20mm x 10mm x 50mm |

Table 2.6 Parameters of the TSAL

### Wiring/cables/connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.  Include gauge, voltage and temperature rating of wiring used and any fuses or other overcurrent protection used.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Measurement points

### Description

Describe the housing used and how it can be accessed, etc.  Describe how the measurement points protected/covered when not in use and how the electrical connections on the back of the measurement points are protected when the measurement points are being used.

| Current limiting resistor Value: |  |
| --- | --- |

### Wiring, connectors, cables

Describe wiring, show schematics, and describe connectors and cables used and show useful data regarding the wiring.  Include details on the protection resistor including resistance, voltage and power rating.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Pre-Charge circuitry

### Description

Describe your concept of the pre-charge circuitry.

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

- Give a plot “Percentage of Maximum Voltage” vs. time

- Give a plot Current vs. time

- For each plot, give the basic formula describing the plots

Additionally, fill out the tables:

| Resistor Type: | for example: ABC Resistor |
| --- | --- |
| Resistance: | for example: 680Ω |
| Continuous power rating: | for example: 60W |
| Overload power rating (1 sec): |  |
| Overload power rating (5 sec): |  |
| Overload power rating (15 sec): |  |
| Voltage rating: | for example: 1500V |
| Cross-sectional area of the wire used: | for example: 0.205 mm² |

Table 2.7 General data of the pre-charge resistor

| Relay Type: | for example: DEF Relay |
| --- | --- |
| Contact arrangment: | for example: SPDT, SPST, SPCO, SPTT, DPST, …. |
| Continuous DC current: | for example: 25A |
| Voltage rating | for example: 2000VDC |
| Nominal Coil Voltage: |  |
| FET type: |  |
| Maximum Drain-Source Current: |  |
| Drain-Source Breakdown Voltage: |  |
| On Charasteristics Gate Threshold Voltage: |  |
| Cross-sectional area of the wire used: | for example: 0.205 mm² |

Table 2.8 General data of the pre-charge relay

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## Discharge circuitry

### Description

Describe your concept of the discharge circuitry.

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables used and show useful data regarding the wiring.

- Give a plot “Voltage” vs. time

- Give the formula describing this behavior

- Give a plot “Discharge current” vs. time

- Give the formula describing your plot

Additionally, fill out the table:

| Resistor Type: | for example: ABC Resistor |
| --- | --- |
| Resistance: | for example: 680Ω |
| Continuous power rating: | for example: 350W |
| Overload power rating (1 sec): | for example: 600W |
| Overload power rating (5 sec): |  |
| Overload power rating (15 sec): |  |
| Voltage rating: | for example: 1500V |
| Maximum expected current: | for example: 0.7A |
| Average current: | for example: 0.3A |
| Cross-sectional area of the wire used: | for example: 0.205 mm² |

Table 2.9 General data of the discharge circuit

| Relay Type: | for example: DEF Relay |
| --- | --- |
| Contact arrangment: | for example: SPDT, SPST, SPCO, SPTT, DPST, …. |
| Continuous DC current: | for example: 25A |
| Voltage rating | for example: 2000VDC |
| Nominal Coil Voltage: |  |
| FET type: |  |
| Maximum Drain-Source Current: |  |
| Drain-Source Breakdown Voltage: |  |
| On Charasteristics Gate Threshold Voltage: |  |
| Cross-sectional area of the wire used: | for example: 0.205 mm² |

Table 2.9 General data of the dis-charge relay

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## HV Disconnect (HVD)

### Description

Describe your concept of the HVD and how it can be operated.

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables and show useful data regarding the wiring.  Include information on the working voltage and current rating of the HVD.

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

## Ready-To-Drive-Sound (RTDS)

### Description

Describe your concept of the RTDS, how is the sound produced, what are the parameters for activating the RTDS, etc.

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables and show useful data regarding the wiring.

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

# Accumulator

## HV Accumulator pack

### Overview/description/parameters

Describe concept of accumulator pack, provide table with main parameters like number of cells, cell stacks separated by maintenance plugs, cell configuration, resulting voltages->minimum, maximum, nominal, currents, capacity etc.

Fill out the following table:

| Maximum Voltage: | for example: 550VDC |
| --- | --- |
| Nominal Voltage: | for example: 500VDC |
| Minimum Voltage: | for example: 300VDC |
| Maximum output current: | for example: 405A for 10s |
| Maximum nominal current: | for example: 250A |
| Maximum charging current: | for example: 50A |
| Total numbers of cells: | for example: 200 |
| Cell configuration: | for example: 100s2p |
| Total Capacity: | for example: 21.6 MJ |
| Number of cell stacks < 120VDC | for example: 5 |

Table 3.1 Main accumulator parameters

### Cell description

Describe the cell type used and the chemistry, provide table with main parameters.

Fill out the following table:

| Cell Manufacturer and Type | for example: Kokam XYZ |
| --- | --- |
| Cell nominal capacity: | for example: 5.4 Ah |
| Maximum Voltage: | for example: 4.2 V |
| Nominal Voltage: | for example: 3.7V |
| Minimum Voltage: | for example: 2.8V |
| Maximum output current: | for example: 20C for 10s |
| Maximum nominal output current: | for example: 15C |
| Maximum charging current: | for example: 5C |
| Maximum Cell Temperature (discharging) | for example: 65°C |
| Maximum Cell Temperature (charging) | for example: 55°C |
| Cell chemistry: | for example: LiFePO4 |

Table 3.2 Main cell specification

### Cell configuration

Describe cell configuration, cell interconnect, show schematics of electrical configuration and CAD of connection techniques, cover additional parts like internal cell fuses etc.

### Cell temperature monitoring

Describe how the temperature of the cells is monitored, where the temperature sensors are placed, how many cells are monitored, etc. Show schematics, cover additional parts, etc.

| Temperature sensor accuracy: |  |
| --- | --- |
| Total number of cells: |  |
| Total number of sensors: |  |
| Max. distance from monitored negative cell terminal: |  |
| AMS opens AIRs during dis-charging if cell temperature is above: |  |
| AMS opens AIRs during charging if cell temperature is above: |  |

### Accumulator Management System

Describe the AMS used including at least the following:

| Minimum cell voltage (shutdown limit): |  |
| --- | --- |
| Maximum cell voltage (shutdown limit): |  |
| Measurement precision (mV): |  |

Table 3.4 Cell voltage limits

- Sense wiring protection (fusing / fusible link wire used)

- What upper and lower voltage does the AMS react at and how does it react?

- What cell temperature does the AMS react at and how does it react?

- Show tables of operation parameters

- Describe how many cells are sensed by each AMS board, the configuration of the cells, the configuration of the boards and how any comms wiring between boards is protected

- Describe how the AMS is able to open the AIRs if any error is detected

- Describe where galvanic isolation occurs between TS and GLV system connections.

### Accumulator indicator

Describe the indicator, show wiring, provide tables with operation, PCB design, etc.

### Wiring, cables, current calculations, connectors

Describe the internal wiring, show schematics, provide calculations for currents and voltages and show data regarding the cables and connectors used.

- Discuss maximum expected current, DC and AC how long will this be provided?

- Compare the maximum values to nominal currents

- Give a table for each kind of wire in your tractive-system:

- Describe your maintenance plugs, provide pictures

- Use tables like the one shown below:

| Wire type | for example: Company A, |
| --- | --- |
| Continuous current rating: | for example: 150A |
| Cross-sectional area | for example: 0.205 mm² |
| Maximum operating voltage: | for example: 800VDC |
| Temperature rating: | for example: 150 °C |
| Wire connects the following components: | for example: Cell and AMS |

Table 3.3 Wire data of company A, 0.205 mm²

### Accumulator insulation relays

Describe the AIRs used and their main operation parameters, use tables, etc.

Additionally, fill out the following table:

| Relay Type: | for example: ABC Relay |
| --- | --- |
| Contact arragment: | for example: SPST |
| Continous DC current rating: | for example: 100A |
| Overload DC current rating: | for example: 200A for 10sec |
| Maximum operation voltage: | for example: 800VDC |
| Nominal coil voltage: | for example: 24VDC |
| Normal Load switching: | for example: Make and break up to 300A |
| Maximum Load switching | 10 times at 1500A |

Table 3.4 Basic AIR data

### Fusing

Describe the fuses used and their main operation parameters, use tables, etc.

Additionally, fill out the following table for each fuse type used:

| Fuse manufacturer and type: | for example: ABC Fuse company, MNO Fuse |
| --- | --- |
| Continous current rating: | for example: 150A |
| Maximum operating voltage | for example: 500VDC |
| Type of fuse: | for example: High speed |
| I2t rating: | for example: 1500A2s at 450VDC |
| Interrupt Current (maximum current at which the fuse can interrupt the current) | for example: 10000A |

Table 3.5 Basic fuse data

Create a table with components and wires protected by the fuse(s) and the according continuous current rating, below is an example table with some potential entries.  Complete this table with information for your design and add/remove additional locations as applicable.  Ensure that the rating of all the components is greater than the rating of the fuse such that none of the other components become the fuse.

| Location | Wire Size | Wire Ampacity | Fuse type | Fuse rating |
| --- | --- | --- | --- | --- |
| Cells to AIRs | 2 AWG | XXX | MNO Fuse | XXX |
| AIR to Motor controller | 0 AWG | XXX | 2x MNO Fuse | XXX |
| AIR to TSAL | 20 AWG | XXX | EFG Fuse | XXX |
| Accumulator output connector | 2 AWG | XXX |  |  |
| Cells to AMS |  |  |  |  |

Table 3.6 Fuse Protection Table

### Charging

Describe how the accumulator will be charged. How will the charger be connected? How will the accumulator be supervised during charging? Show schematics, CAD-Renderings, etc., if needed

Additionally, fill out the table:

| Charger Type: | for example: ABC Charger |
| --- | --- |
| Maximum charging power: | for example: 3kW |
| Maximum charging voltage: | for example: 550V |
| Maximum charging current: | for example: 20A |
| Interface with accumulator | for example: CAN-Bus, proprietary, serial communication... |
| Input voltage: | for example: 230 VAC |
| Input current: | for example: 16A |

Table 3.7 General charger data

### Mechanical Configuration/materials

Describe the concept of the container, show how the cells are mounted, use CAD-Renderings, show data regarding materials used, etc.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.  Ensure that the required mechanical structure to protect the accumulator and other electrical components is clearly identified.

## GLVS Accumulator

### Description

Describe your concept of the GLVS Accumulator.

| Cell/Accumulator: |  |
| --- | --- |
| Accumulator configuration – parallel: |  |
| Accumulator configuration – series: |  |
| Maximum Voltage: |  |
| Nominal Voltage: |  |
| Minimum Voltage: |  |
| Max. Continuous Discharge Current: |  |
| Peak Discharge Current: |  |
| Peak Discharge Current Time: |  |
| Max. Continuous Charge Current |  |
| Total capacity[MJ]: |  |

### Wiring, cables, current calculations, connectors

Describe wiring, show schematics, describe connectors and cables and show useful data regarding the wiring.  Include information on the working voltage and current rating of the accumulator.

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

# Energy meter mounting

## Description

Describe where the energy meter is mounted and how, etc.

## Wiring, cables, current calculations, connectors

Describe the wiring, show schematics, provide calculations for currents and voltages, and show data regarding the cables and connectors used.

## Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

# Motor controller

## Motor controller 1

### Description, type, operation parameters

Describe important functions; provide table with main parameters like resulting voltages->minimum, maximum, nominal, currents etc.

Fill out the following table:

| Motor controller type: | for example: ABC Controller |
| --- | --- |
| Maximum continous power: | for example: 60kW |
| Maximum peak power: | for example: 75kW for 10s |
| Maximum Input voltage: | for example: 600VDC |
| Output voltage: | for example: 250VAC |
| Maximum continuous output current: | for example: 100A |
| Maximum peak current: | for example: 200A for 5s |
| Control method: | for example: PWM, analog signal... |
| Cooling method: | for example: Air, water, oil... |
| Auxiliary supply voltage: | for example: 24VDC |

Table 5.1 General motor controller data

### Wiring, cables, current calculations, connectors

Describe the wiring, show schematics, provide calculations for currents and voltages and show data regarding the cables and connectors used.

Additionally, fill out table:

| Wire type: | for example: Company A, 0.205 mm² |
| --- | --- |
| Current rating: | for example: 150A |
| Fuse current rating: |  |
| Maximum operating voltage: | for example: 800V |
| Temperature rating: | for example: 150 °C |

Table 5.2 Wire data of company A, 0.205 mm²

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## Motor controller 2

…

If identical parts are used, just refer to the corresponding sections, don’t copy and paste.

.

# Motors

## Motor 1

### Description, type, operating parameters

Describe the motor used, provide table with main parameters like resulting voltages->minimum, maximum, nominal, currents, resulting motor power, use figures to show important characteristics.

Additionally, fill out table:

| Motor Manufacturer and Type: | for example: ABC Motor |
| --- | --- |
| Motor principle | for example: Asynchronous, permanently excitated |
| Maximum continuous power: | for example: 25kW |
| Peak power: | for example: 70kW for 5s |
| Input voltage: | for example: 250VAC |
| Nominal current: | for example: 50A |
| Peak current: | for example: 70A |
| Maximum torque: | for example: 60Nm |
| Nominal torque: | for example: 20Nm |
| Cooling method: | for example: Water, oil, air,... |

Table 6.1 General motor data

- Give a plot of power vs. Rpm including a line for nominal and maximum power

- give a plot of torque vs. rpm including a line for nominal and maximum torque

### Wiring, cables, current calculations, connectors

Describe the wiring, show schematics, provide calculations for currents and voltages and show data regarding the cables and connectors used.

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary and clearly identify the structure used to protect all relevant parts.

## Motor 2

…

If identical parts are used, just refer to the corresponding sections, don’t copy and paste.

# Torque encoder

## Description/additional circuitry

Describe the type of the torque encoder(s) used, provide tables with main operation parameters, and describe additional circuitry used to check or manipulate the signal going to the motor controller. Describe how the system reacts if an implausibility or error (e.g. short circuit or open circuit or equivalent) is detected.

| Torque encoder manufacturer: | for example: ABC Encoder |
| --- | --- |
| Torque encoder type: |  |
| Torque encoder principle: | for example: potentiometer |
| Total number of Torque Encoder Sensors: |  |
| Supply voltage: | for example: 5V |
| Maximum supply current: | for example: 20mA |
| Operating temperature: | for example: -20..180 °C |
| Used output: | for example: 0-5V |

Table 7.1 Torque encoder data

## Torque Encoder Plausibility Check

Describe additional circuitry used to check or manipulate the signal going to the motor controller. Describe how failures (e.g. Implausibility, short circuit or open circuit or equivalent) are detected and how the system reacts if an implausibility or errors is detected.

## Wiring

Describe the wiring, show schematics, show data regarding the cables and connectors used.

## Position in car/mechanical fastening/mechanical connection

Provide CAD-renderings showing all relevant parts and discuss the mechanical connection of the sensors to the pedal assembly. Mark the parts in the rendering, if necessary.

# Brake encoder

## Description/additional circuitry

Describe the type of the Brake system encoder(s) used for regenerative braking (if any).

| Brake encoder manufacturer: | for example: ABC Encoder |
| --- | --- |
| Brake encoder type: |  |
| Brake encoder principle: | for example: potentiometer |
| Total number of Brake Encoder Sensors: |  |
| Supply voltage: | for example: 5V |
| Maximum supply current: | for example: 20mA |
| Operating temperature: | for example: -20..180 °C |
| Used output: | for example: 0-5V |

Table 7.1 Brake encoder data

## Brake Encoder Plausibility Check

Describe additional circuitry used to check or manipulate the signal going to the motor controller. Describe how failures (e.g. Implausibility, short circuit or open circuit or equivalent) are detected and how the system reacts if an implausibility or errors is detected.

## Wiring

Describe the wiring, show schematics, show data regarding the cables and connectors used.

## Position in car/mechanical fastening/mechanical connection

Provide CAD-renderings showing all relevant parts and discuss the mechanical connection of the sensors to the pedal assembly. Mark the parts in the rendering, if necessary.

# Additional LV-parts interfering with the tractive system

## LV part 1

Describe those parts here which interfere or influence the tractive system, for example a controlling unit that measures wheel speeds and steering angle and calculates a target torque for each motor or a DC/DC-Converter providing power for the LV-system from the HV-system, etc.

### Description

Describe the parts used and their circuitry, and provide main operation parameters, use tables or figures, etc.

### Wiring, cables,

Describe the wiring, show schematics, etc.

### Position in car

Provide CAD-renderings showing the relevant parts. Mark the parts in the rendering, if necessary.

## LV part 2

…

# Overall Grounding Concept

## Description of the Grounding Concept

Describe how you intend to achieve the resistances between components at the required levels as defined in EV4.3.

## Grounding Measurements

Describe which measurements you will take to ensure that EV4.3 is achieved

# Firewall(s)

## Firewall 1

### Description/materials

Describe the concept, layer structure and the materials used for the firewall. Show how the low resistance Control System ground connection is achieved.

### Position in car

Provide CAD-renderings showing all relevant parts. Mark the parts in the rendering, if necessary.

Firewall 2

# Appendix

Numbering according to chapter 1 to 10

A datasheet for motor controller one for example has to have the numbering 11.10.5

Example appendix entry:

11.2.2 – Bender IR155-3203 IMD ratings

Referred from 2.1.1.

Complete data sheet located at: 
http://www.bender-de.com/fileadmin/products/doc/IR155-32xx-V004_DB_en.pdf